Preliminaries:

This software suite registers sequences of 3D image stacks for analysis. While it was built for developing C. elegans embryos, it would probably work on other types of image data as well – any type of sample that is confined in space and does not move too quickly – with some modifications.
The Matlab-based registration program (entry-point: RegistrationWrapper / MainRegister) anticipates image data in two segmentation channels: first, an alignment marker which is relatively stable in its distribution around the AP-axis of the animal over time, and importantly, also stable in absolute position between stacks – in our case, this marker is unc-130::GFP-labeled nuclei; second, a marker representing all nuclei in the animal, which can be used for staging embryos and finding their overall structure / outline – in our case, this is the histone mCherry marker. The alignment marker segmentation data should be in h5 format, with values between 0 and 1 for every pixel describing the confidence of the labeling. In our case this data was generated using the program Ilastik, as described in the text. The pan-nuclear marker must be in the specific format generated by StarryNite: in other words, the data is presented in the form of a structure array (array index is over time) “esequence” which contains an array called “finalpoints” for each time point, defining all segmented nuclear centers for that time point. These centers could easily be generated in some other way provided they are input to the Matlab program in the correct format.

The particular names of the input files for Starry Nite and the Matlab registration pipeline are important.

StarryNite (in our version) requires a sequence of .mat 3D matrix stacks named e.g. 4_0001.mat, 4_0002.mat, where 4 refers to the position, and 1, 2 refer to the stack number.

Some example input files for our Matlab registration program follow:

Btc_Ds2_Pos4_Co0_St25.Tiff

Btc_Ds2_Pos4_Co0_St25Probabilities.h5

2_4_emb1_fullmatlabresult.mat

The nomenclature is as follows. “Btc” is short for “bleed-through-correct” it is coded as an “input_prefix” in the Matlab program. Ds2 refers to dataset 2; Pos4 is position 4; Co0 is color 0 (green in our case; 1 is used for the red channel); St25 is stack 25. The first file is an image stack, and the second file is an array of probability matrices of the same size as the tiff file, with dimensions [x,y,z,c], where c is the segmentation channel. 2_0_emb1_fullmatlabresult is the output of a StarryNite segmentation run. With one correctly named fullmatlabresult file per embryo, and one tiff Stack / probability array per time point per embryo, the program will run to carry out registrations. Each embryo’s files should be placed in a separate directory.

The Matlab software has been tested in version 2015a and requires the Image Processing addon to work correctly.

The StarryNite program can be obtained from here (https://sourceforge.net/projects/starrynite/files/starryniteII/). We tested our Matlab software using a pre-release version of StarryNite II; while it is unlikely, if there are any problems arising from incompatibility between the present StarryNite distribution and the one we use, please feel free to copy our distribution (present on this server -- slightly modified from its original version by us).

Additionally, Ilastik can be downloaded here (http://ilastik.org/) – our program was tested using Ilastik version 1.1.5.

Instructions:

These instructions are written for a user running the program on data similar to our own. See other sections in this guide for a few suggestions on how to broaden the usage to other cases. Contact Peter Insley with specific questions (peter.insley@gmail.com).

The order of operations is:

1) Collect image data, a sequence of stacks, for multiple embryos which have been approximately identically staged. The data should be well-sectioned for best performance (such as is the data produced on our SPIM microscope). Convert the raw image data of whatever original format into separate Tiff stacks (see SimplyStacks program for some suggestion on how to do this in Matlab, starting from individual Tiff images).

2) Resize the image stacks to fit the embryos as closely as possible without losing information (perhaps using ResizeMovies). While input image data can be of any size, being conservative here will drastically reduce processing time / RAM usage. The latter especially might become prohibitive for large stacks. In our case the image stacks were 351 x 251 x 93 (interpolated to 287) voxels in size. The Z interpolation factor is set in MainRegister, and should be set (depending on slice spacing) to produce symmetrical voxels.

3) Run BleedThroughCorrect with suitable modifcations. In our case it was only necessary to subtract green bleedthrough from the red channel, the reverse being negligible. In other cases: either simply adjust the multiplier to suit the particular optical system / fluorophore; or, in the case that both red bleedthrough into green and green bleedthrough into red are appreciable, invert a matrix to find the right linear combination of images to subtract. It may be necessary to take images under identical imaging conditions of the separate green and red markers – for instance, of separate strains prior to crossing – to determine how much of a given image is due to bleedthrough and how much from actual signal.

4) Run the StarryNite program to segment the pan-nuclear channel. StarryNite expects Matlab matrix input for image data (see TiffStacktoStarryNiteStack for an indication of how to do this, starting from Tiff stacks). In our case we used Starry Nite to segment only the first 40 stacks – MainRegister is set by default (parameter “last_moment_stack” to only use StarryNite stacks in reference up to stack 30, and to never go beyond stack 40 in test embryos (parameter “last_starry_nite_stack). The exact range of StarryNite stacks considered for a given embryo depends on the calculated temporal offset.

5) Use Ilastik or similar (see preliminaries section above) to produce h5 segmentation data for the alignment marker. We ran Ilastik on the original (93) slice files: this was not ideal, as these files do not have symmetrical voxels and the version we used reportedly did not have the capacity to produce asymmetrical (elliptical) classifiers; on the other hand, it led to substantial performance improvements and did not seem to cause any issues with the ultimate segmentation.

6) Choose a reference embryo. There are not many requirements here, but ideally the reference embryo should be a not too out-of-the-ordinary embryo in its staging (if possible, not the youngest embryo in the dataset, or the oldest). C. elegans embryos are perturbed by aggressive imaging; do not use a damaged embryo for the reference. In our case we had observed the reference embryo to hatch, and so we knew it had not been especially damaged by the imaging.
7) Adjust parameters / filenames / directory data in RegistrationWrapper and MainRegister. RegistrationWrapper is used to loop over many embryos. MainRegister runs at most one reference and one test embryo and corresponds to the “main” part of the program. The best way to run these two together is: first, run MainRegister for the reference embryo alone; then afterwards, loop over the entire test embryo population without re-registering the reference. While there are many parameters in MainRegister (all saved to disk in a textfile and also as a structure, as “reg params”), the important ones are listed below (some overwrites for the test parameters are available in RegistrationWrapper, labeled “external”). “Moving” and “target” below correspond to “test” and “reference” in the paper.

Parameters describing the image geometry, timing, and segmentation channels:

optreg.num_segmentation_variables: the number of segmentation channels in the h5 segmentation.

optreg.background_segmentation_variable, optreg.nuclei_segmentation_variable, optreg.emb_background_segmentation_variable, optreg.cell_body_segmentation_variable, optreg.neurite_segmentation_variable: These define the different available segmentation channels in the h5 file. Of these, nuclei_segmentation_variable (describing the channel where the unc-130 nuclear segmentation is located – 2, in our case) is the channel where the alignment marker data is segmented.

optreg.z_multiplier: the interpolation factor in Z for the original slices (3.077 in our case).

optreg.img_width: the width of the images in pixels.

optreg.img_height: the height of the images in pixels.

optreg.num_slices: the number of slices in the original Z-stack.

optreg.new_frame: [X,Y,Z] where Z is the interpolated number of slices – 3.077 times num_slices, in our case.

optreg.center_position: The center of the new frame. Calculated in the program (i.e. [176, 126, 144] in our case).

optreg.moving_x_bounds, optreg.moving_y_bounds, optreg.target_x_bounds, optreg.target_y_bounds: If StarryNite runs were conducted on a full image (before ResizeMovies was applied), these bounds define where the cut out was made and provide a necessary offset to the StarryNite segmentation. Otherwise, enter the full range for the image.

optreg.first_moving_stack, optreg.last_moving_stack, optreg.first_target_stack, optreg.last_target_stack: The first and last stack numbers in each registration sequence.

Parameters describing the file identification / nomenclature / foldering / time stamping:

optreg.input_prefix: Defines any input prefix on the files (e.g. “Btc_”, which stands for “bleed-through-correct).

optreg.moving_dataset_directory: The directory where the image, segmentation, and emb_result files are located.

optreg.moving_dataset: The dataset number of the embryo. This can be overwritten by RegistrationWrapper.

optreg.moving_position: Datasets are divided into position numbers (for multi-position single imaging experiments). This can be overwritten by RegistrationWrapper

optreg.moving_strain_name: Optional strain name to distinguish experiments (e.g. “NG_”). This can be overwritten by RegistrationWrapper.

optreg.moving_strain_number: Used for indexing into arrays containing parameters for all strains in RegistrationWrapper. For instance, in our case, wild type is strain number 1, cam-1 strain number 2.

optreg.moving_run_number: The run number for this dataset, position (in case multiple runs with different parameters are required). This can be overwritten by RegistrationWrapper.

optreg.moving_moments_time: The time when the transform matrix and associated files were calculated. Either generated from the computer’s datetime or inserted by the user to load pre-existing matrices.

optreg.start_time: The time when the main part of the registration was run. Stamped on all generated files (along with all other identifying features). Either generated from the computer’s datetime or inserted by the user to load pre-existing matrices / files.

Identical, symmetrically named parameters exist for the reference, with “target” substituted for “moving”; the exception to this being start_time, where the reference version is named “optreg.target_start_time”.

Parameters beginning beginning with “calculate” or “use.”

calculate_moments_moving: Whether to run the moments / ellipsoids portion of the program for the test embryo. If set to true, the program will calculate a transform matrix and associated matrices for the test. If set to false, the program will look for a transform matrix with suitable run number / time stamp on disk, and throw an error if it cannot find one.

optreg.calculate_moving_reg: Whether to calculate the self-registrations for the test embryo. If true, obviates use_existing_mov_reg.

optreg.use_existing_mov_reg: Whether to load in self-registrations from disk for the test embryo. If the program cannot find anything with the correct time stamp / other identifiers, throws an error. If this and calculate_moving_reg are both false, the program will attempt to do without moving embryo registrations (so-called one-sided registration, operating only on the reference side).

optreg.calculate_indirect_cross_reg: Whether to do the initial cross registration step. If true, obviates use_existing_indirect_cross_reg.

optreg.use_existing_indirect_cross_reg: Whether to load existing cross registration matrices from disk.

optreg.refine_alignments: Whether to carry out the 3D refinement step described in the paper, after basic alignment is complete. (There is no “use” version of this, since it is in any case the last alignment step.)

Identical, symmetrically named parameters exist for the reference for some of the above, with “target” substituted for “moving”; the exceptions are the “cross” and “refine” parameters.

optreg.two_sided_reg: True/false, calculated in the program, based on the values of the above parameters. Describes whether the run is one- or two-sided.

Parameters describing the run conditions:

optreg.alignment_method: Can be “moments” or “ellipsoids.” Describes how embryo axes are determined (whether by convex hull / moments of inertia or by min vol ellipse). We always ran with “moments,” except when running with ellipsoids for comparing the initial alignment steps by the two methods.

optreg.scaling_method: How the embryo scaling is carried out. Can be “moments,” “moments_projection,” “ellipsoids,” or “no_scaling.” Moments_projection is a less principled version of moments (described in the paper). Ellipsoids scales based on the min vol ellipse. We always ran with “moments,” except when running with ellipsoids for comparing the initial alignment steps by the two methods.

optreg.register_compose_type: Whether to go frame by frame in self registration (“short_jumps”),
 to register to a target a few frames away (“long_jumps”), or to average over several short_jump spaced long_jump sequences (“short_and_long_jumps”). We always used “short_jumps”.

optreg.register_moving_forward, optreg.register_target_forward: Booleans that describe whether the self registration sequences go towards the end or towards the beginning of the sequences. We always used backward registration (false) for the test embryo and forward registration (true) for the reference.

optreg.cross_map_last_time_point: Whether all images are mapped to the first or last time point in the reference sequence. Always true in our case.

optreg.nuclei_2D: Whether to run the self registrations in 2 or 3D. True in our case.

optreg.nuclei_fix_centroid: Whether to fix the centroids in the self registrations. True in our case.

optreg.do_theta, optreg.do_emb_background_reg, optreg.only_calculate_direct_last, optreg.cpd_normalize, optreg.second_round_nuclear, optreg.third_round_nuclear: Keep these parameters false. They have not been tested with recent versions.

optreg.unfix_cross_reg_centroids: Whether to permit centroids to fluctuate in the cross registrations. True in our case.

optreg.glue_first_to_first, optreg.glue_last_to_last: Whether to force the first stack in the test sequence to register to the first stack in the reference; whether to force the last stack in the test to register to the last stack in the reference sequence. If both are true, then no time offset is done. We set glue_last_to_last to true, since we want to compare the ends of runs at twitching (a definite last time point for the series). Glue first to first was set to false, thus time offsetting would result in pushing the first stack in the sequence either in reference or in test.

optreg.offset_initial_reg_time_point: Whether to apply the time offset to adjust the first stack in the test / registered sequence. Only runs if glue_first_to_first is false. Set to true in our runs. If glue first to first, but no offseting, then the program fixes the first stack for both sequences to the higher of first_target_stack and first_moving_stack.

optreg.offset_final_reg_time_point: Whether to apply the time offset to adjust the first stack in the test / registered sequence. Only runs if glue_last_to_last is false. Set false in our runs. If glue last to last, but no offseting, then the program fixes the last stack for both sequences to the smaller of first_target_stack and first_moving_stack.

optreg.fix_total_number_stacks: Whether to force the total number of stacks in the sequence to be the same in reference and test. Not well tested. May conflict with providing time offsets. Always kept false in our case.

Settings that can be overwritten from RegistrationWrapper:

optreg.moving_x_bounds, optreg.moving_y_bounds: Program searches first for a cell array in the workspace called “bounds”.

optreg.moving_moments_time: Program searches first for a cell array in the workspace called “moments_times”.

optreg.moving_dataset: Program searches first for a cell array in the workspace called “datasets”.

optreg.first_moving_stack, optreg.last_moving_stack: Program searches first for a cell array in the workspace called “stacks”.

optreg.start_time: Program searches first for a cell array in the workspace called “moving_start_times”.

optreg.moving_position: Program searches first for a variable in the workspace called “external_specified_position”.

optreg.moving_dataset_directory: Program searches first for a variable in the workspace called “external_specified_dataset_directory”

optreg.moving_run_number: Program searches first for a variable in the workspace called “external_specified_run_number”.

optreg.moving_strain_number: Program searches first for a variable in the workspace called “external_specified_strain_number”.

optreg.moving_strain_name: Program searches first for a variable in the workspace called “external_specified_strain_name”.

Parameters beginning with “show”, “save”, or “demo”:

These define which files to show (in the Matlab window, as figs) or to save to disk. The default settings should be fine for most users.

8) Run the program. The fully registered test stacks are saved in “Run [run number]/ CrossRegIms/corrected” in the moving dataset directory, while the fully registered reference stacks are saved in “Run [run number]/SelfRegIms” in the reference dataset directory.

9) Analyze data / inspect registered data. We don’t provide a pipeline for doing this (aside from a few graphing utilities). Most of our analysis was done by hand, but additional pipelines involving e.g. automated neurite segmentation could be hooked into the one described here.

Additional notes:

The program expects that stacks 1-20 will have time intervals five times the length of later intervals – e.g., in the paper, stacks 1-20 were carried out with 10 minute intervals between stacks, while later stacks were at 2 minute intervals. These timing assumptions can be modified with minimal difficulty in the source code. The program expects to have at least two embryo sequences taken with identical timing, roughly identically staged (within an hour for C. elegans embryos is fine) for registration.

In our runs, all test embryos were registered onto one reference embryo chosen roughly at random (up to considerations described above); however, other registration schemes could probably be developed using the code here as a base. What is required however is the “moving / target” scheme; it would be difficult to implement registration onto a mean target embryo using this code. Intermediate reference embryos might work (this might be useful in some hierarchical clustering scheme).

In our case, the unc-130::GFP labeling is segmented out using Ilastik from other labeling in the GFP channel – however, this is not necessary in all cases. For example, if unc-130 is the only label in the green channel while neurons / cell bodies are labeled in other colors, it might not be necessary to segment the green channel in the first place beyond a simple thresholding (which provides the required [0 1] probability labeling for each pixel).